Download Quartus II Web Edition : https://www.altera.com/download
- Depending on your Altera FPGA device, select a version (for example, the latest free version that supported Cyclone II was Quartus 13.0 SP1)
- You don’t need to have an FPGA device to play with this design – ModelSim would do just fine!
Download ModelSim for Altera from the same site.
Presumably you have already downloaded A-Z80 project : https://bitbucket.org/gdevic/a-z80
You can select any folder for your git repo; this document assumes it is in C:\fpga\A-Z80
Install Python: http://www.activestate.com/activepython

How do I run a whole-chip simulation?

Run “modelsim_setup.py” to prepare ModelSim paths

In the folder as shown below, open “test_host.mpf” in ModelSim (double-clicking should open it if properly installed)

Type command: vlib work

Compile All…

Start a simulation configuration “test_host”

Open the Wave window (if it is not already there): Menu: View -> Wave
In the Wave window, open a wave file “wave_host.do”

In general, each ModelSim simulation configuration contains a wave file with the same name.

Start the simulation run

After a few seconds, stop the simulation run

You should be able to examine all the signals in the wave window

Your Transcript window should also show the result of this simulation (“Hello, World!”)

How do I restart a simulation?

Every ModelSim project contains a macro file “r” which you can run by typing “do r” in your ModelSim Transcript window. This macro contains simple command to restart a simulation (“restart -f ; run -all”).

How do I change the Z80 software that runs in ModelSim?

There are 2 ModelSim projects that can run Z80 code:
1. Host board: \fpga\A-Z80\host\toplevel\simulation\modelsim (described in the previous section)
2. CPU only: \fpga\A-Z80\cpu\toplevel\simulation\modelsim

Z80 code is the folder “zmac”.

ModelSim host board simulation contains simulated UART, RAM, ROM. It loads “fpga.asm” which is compiled by “make_fpga.bat” file. It contains a complete image which is loaded at the address 0 and run.

ModelSim CPU only simulation uses “boot.asm” which is compiled by “boot.bat”. It provides a boot code that loads at the address 0 and executes first. This Z80 code then jumps to the address 0x100 where is the execute code - one of the ones (*.asm) in the pink as shown:

You can add your own or modify one of the existing ones. Compile it by simply dragging and dropping the ASM source file onto the “exec.bat” batch file through the Windows explorer.

The batch file will compile it and move the object code to the proper ModelSim directory after which you need to recompile a ModelSim project and then you can re-run it (“do r”).

How do I add my own FPGA board?

Currently 2 boards are supported – I just happen to have those two and they are called:
1. RedCore
2. RioRand

In the host folder, open the board project “host_board.qpf” in Quartus (double-clicking should open it if properly installed)

Those 2 boards are stored as revisions. See them in Project->Revisions. Both of them have Altera Cyclone II FPGA.
You can add your own board either by adding another revision, or simply by modifying the current default board.

You need to specify your exact FPGA model in Assignments->Device dialog.

If you want to use the default Z80 boot code, you will need a board with an UART. In your board’s documentation, find the pins on FPGA for these signals:

Signal	FPGA pin on “RedCore”	FPGA pin on “RioRand”	FPGA pin on your board
clk (50 MHz)	23	17
Reset button	27	144
UART_TX	15	73

Plug in those pin numbers in the pin editor menu Assignments->Pin Planner.
Recompile the design by Processing->Start Compilation.
Program the device by Tools->Programmer.