A-Z80 Quick Start
Download Quartus II Web Edition : https://www.altera.com/download
- Depending on your Altera FPGA device, select a version: the latest free version that supported Cyclone II was Quartus 13.0 SP1, so if you intend to run ZX Spectrum on DE1 board, you need to use that version.
- You don’t need to have an FPGA device to play with this design – ModelSim would do just fine!
Download ModelSim for Altera from the same site.
Presumably you have already downloaded A-Z80 project : https://bitbucket.org/gdevic/a-z80
Install Python: http://www.activestate.com/activepython

How do I setup my Altera DE1 board to run Sinclair ZX Spectrum?

You need to flash ZX Spectrum ROM into the flash memory at the address 0. Use the program “DE1_ControlPanel.exe” which is on your DE1 CD disk (which you can download from terasic.com site).

The file to flash is a combined ROM “host\zxspectrum\rom\combined.rom”.

Open “host/zxspectrum/zxspectrum_board.qpf” project file in Quartus, compile it and download onto your Altera DE1 board. Connect VGA, PS/2 keyboard and line-in to load Spectrum programs. You can also connect Line-out to hear the sounds (plugging in a set of earphones would also do).

How do I run a whole-chip simulation?

Run “modelsim_setup.py” to prepare ModelSim paths:

In the folder as shown below, open “test_host.mpf” in ModelSim (double-clicking should open it if properly installed)

Type command: vlib work

Compile All…

Start a simulation configuration “test_host”

Open the Wave window (if it is not already there): Menu: View -> Wave
In the Wave window, open a wave file “wave_host.do”

In general, each ModelSim simulation configuration contains a wave file with the same name.

Start the simulation run

After a few seconds, stop the simulation run

You should be able to examine all the signals in the wave window

Your Transcript window should also show the result of this simulation (“Hello, World!”)

How do I restart a simulation?

Every ModelSim project contains a macro file “r” which you can run by typing “do r” in your ModelSim Transcript window. This macro contains simple command to restart a simulation (“restart -f ; run -all”).

How do I change the Z80 software that runs in ModelSim?

There are 2 ModelSim projects that can run Z80 code:
1. Host board: host\toplevel\simulation\modelsim (described in the previous section)
2. CPU only: cpu\toplevel\simulation\modelsim

Z80 code to assemble is in the folder “zmac”. Drag and drop any of the *.asm source files onto “make_modelsim.bat” and the batch file will assemble it and copy to proper ModelSim folders to be loaded for simulation after which you need to recompile a ModelSim project and then re-run it (“do r”).