A-Z80 Quick Start
Download Quartus II Web Edition: https://www.altera.com/download
Depending on your Altera FPGA device, select a version: For the DE1 board, the latest free version that supported Cyclone II was Quartus 13.0 SP1.
Download ModelSim for Altera from the same site.
You don’t need to have an FPGA device to play with this design – ModelSim could do just fine to test and run various simulations!
Xilinx devices should work by linking with Verilog/SystemVerilog files, but I did not try it.
Install Python 2.x: http://www.activestate.com/activepython

How do I setup my Altera DE1 board to run Sinclair ZX Spectrum?

Flash ZX Spectrum ROM package (provided) into the flash memory at the address 0. Use the program “DE1_ControlPanel.exe” off your DE1 CD disk (you can also download it from the terasic.com site).

The file to flash is a combined ROM “host\zxspectrum\rom\combined.rom”.

Open “host/zxspectrum/zxspectrum_board.qpf” project file in Quartus, compile it and download onto your Altera DE1 board. Connect VGA, PS/2 keyboard and line-in to load Spectrum programs. You can also connect Line-out to hear the sounds (plugging in a set of earphones would also do). Use the Line-in jack on your Altera board to load programs.

How do I add A-Z80 sources into my Z80-based project?

You can look up a list of files that were added to one of the sample designs:
1. “host\basic\host_de1.qsf” (or *.qpf)
2. “host\zxspectrum\zxspectrum_board.qsf” (or *.qpf)
Simply copy their configuration by copying every file from the “cpu” directories listed. Needless to say, be sure to close timings on your design or it may not work reliably.

The A-Z80 CPU is implemented through a combination of schematic files and SystemVerilog files. I have compiled schematic files into simple Verilog files and those are to be included. Therefore, the design should work on Xilinx development setups as well, but I did not test that since my boards are all Altera.

How do I make CPU modifications and compile it?

That’s a great question! 
This is the process of building the A-Z80 CPU from scratch.

If you are making any instruction sequence/timing changes, open the file “cpu\control\Timings.xlsm” in Microsoft Excel. That file contains timing tables for each instruction group. Vertical columns are operations on specific blocks. Instruction groups are listed by the M and T clock providing the exact timing for each set of operations.

Operations itself are represented by short tokens (for example, “PC” or “mr”, etc.) which are defined in the file “cpu\control\timing_macros.i”. Look it up and you will see every token defined and translated into one or more concrete control signals.

After you change the timing spreadsheet export it into a TAB-separated file. The spreadsheet contains a macro to do that. Click on the “Developer” menu and run the Macros:

This will replace the existing CSV file which is ok.

Now we need to create the actual Verilog file from those timings. A python script “cpu\control\genmatrix.py” is used to create “exec_matrix.i” file which implements Verilog code that controls the timing. Run the Python script in-place, no arguments are necessary.

If you make a schematic change which adds or removes module signals, you need to run those two Python scripts to recreate global includes:
“cpu\control\genref.py”
“cpu\toplevel\genglobals.py”

Various Quartus projects that are in “cpu\alu”, “cpu\bus”, “cpu\control” and “cpu\registers” are non-functional and just conveniently hold sets of files. Project in “cpu\toplevel” contains top-level schematic diagram only. It is also not functional in this release – in order to compile a project, look in a sample project such is “host\basic”.

If you are modifying a module that is designed through a schematic (which are most of the A-Z80 blocks), open one of the Quartus projects for that module (for example, “cpu\alu\test_alu.qpf”), change the schematics, compile it (to make sure it has no errors) and then export it to both the Verilog equivalent and a symbol file as shown below. Verilog code will be used to compile with the rest of the A-Z80 files in your master top-level design project while the symbol file is optional for now but could be used in the future to create a schematic top-level.

Still stuck?

Visit www.baltazarstudios.com, post a question and/or send me an email.

Goran Devic
gdevic @ yahoo.com